Drawing pad vs. Mouse pad

Installing version .84 of Sugar

In order to enable the drawing pad, the XO must be running version .84 of Sugar, which is being developed and test in Paraguay.

It can be obtained from here:

 http://people.sugarlabs.org/bernie/olpc/f11-xo1-py/

The files you need are os180py.img and os180py.crc. Once you have them on a USB stick, you can reflash laptops by pressing a (X / esc) key at boot time to drop into the Open Firmware. When you get the "ok" prompt, type the following command:

copy-nand u:\os180py.img and press (ENTER)

and reboot the XO.

This is the ParaguayEduca image, so the Browse comes customized, but you can just delete and install the regular Browse activity from the wiki.laptop.org page

Changing mode from the “terminal” activity

(1) to enable:

su –l

echo 'options psmouse ptmode=1' > /etc/modprobe.d/ptmode.conf

and reboot the XO

The drawing pad requires a little bit of pressure. You can use the back of a pen, but PLEASE do not write on the pad.

(2) to disable:

su –l

rm /etc/modprobe.d/ptmode.conf

and reboot the XO

# Footnotes

This procedure works if the XO is unsecured, which means that it does not require a activation key.